## Slide 1: Filtering in the Frequency Domain
Mr. ANWAR KHAN
Dept. of Computer Science
University of Lahore

## Slide 2: Objectives
This lecture reviews frequency domain filtering.
  Frequency bands
  Lowpass filter
    Ideal, Butterworth, Gaussian
  Highpass filter
    Ideal, Butterworth, Gaussian

## Slide 3: Basic Steps

## Slide 4: Basics
Steps for filtering in the frequency domain
Input: M × N image f(x, y) Output: M × N image g(x, y)
Padded images: P × Q images fP (x, y) and gP (x, y) (P = 2M , Q = 2N )
Zero pad f(x, y) ⇒ fP (x, y)
Multiply fP (x, y) by (−1)(x+y)
Compute F (u, v), that is the FT of the result in (2)
Multiply F (u, v) by H(u, v) (array multiplication)
Compute the IFT of the result in (4)
Obtain the real part of the result in (5)
Multiply the result in (6) by (−1)(x+y) ⇒ gP (x, y)
Crop gP (x, y) ⇒ g(x, y)

## Slide 5: The Discrete Fourier Transform (DFT)
1. Given an image f(x,y) or size MxN
x = 0, 1, 2…M-1
y = 0,1,2…N-1
2. Discrete Fourier Transform of f(x, y) is given by
u = 0, 1, 2…M-1
v = 0, 1, 2…N-1
j= sqrt(-1)
N
M
Origin

## Slide 6: The Inverse DFT
The key feature of a Fourier Transform is that it’s completely reversible
The inverse DFT is given by:
x = 0, 1, 2…M-1
y = 0, 1, 2…N-1

## Slide 7
The Inverse DFT

## Slide 8: Frequency Bands
Low frequencies: general graylevel appearance over smooth areas: slowly varying grayscales.
High frequencies: responsible for detail, such as edges and noise.
A filter that attenuates high frequencies while “passing” low frequencies is a lowpass filter.
A filter that attenuates low frequencies while “passing” high frequencies is a highpass filter.
Lowpass filters blur images.
Highpass filters highlight edges.

## Slide 9: Lowpass and Highpass Filters
Lowpass filter
Highpass filter

## Slide 10: 1. Low-pass Filters
Attenuates high frequencies and retains low frequencies unchanged.
  high frequencies correspond to sharp intensity changes
The result in the spatial domain is equivalent to that of a smoothing filter
  fine-scale details and noise in the spatial domain image are filtered

## Slide 11: Ideal Lowpass Filter
cutoff frequency

## Slide 12: The transfer function for the ideal low pass filter can be given as:
Ideal Low Pass Filter

## Slide 13: Butterworth Lowpass Filter (BLPF)
H (u, v) 
0
1  [D(u, v) / D ]2n
1
n is filter order

## Slide 14: Gaussian Lowpass Filter (GLPF)
2
0
2
 D (u ,v) / 2 D
H (u, v)  e
σ = D0 = cutoff freq

## Slide 15: 1. High-pass Filters
Attenuates high frequencies and retains low frequencies unchanged.
  high frequencies correspond to sharp intensity changes
The result in the spatial domain is equivalent to that of a smoothing filter
  fine-scale details and noise in the spatial domain image are filtered

## Slide 16: High-pass Filters
A highpass filter yields edge enhancement or edge detection in the spatial domain
Edges contain mostly high frequencies while other areas of the image are rather constant gray level (i.e. low frequencies) which are suppressed.

## Slide 17: Highpass Filters: 1-HLP
Butterworth highpass filter
Gaussian highpass filter


0
1 if D(u, v)  D0
Ideal highpass filter
0 if D(u, v)  D
H (u, v) 
2n
H (u, v) 
0
1
1 D D(u, v)
0
2 2
 D (u ,v) / 2 D
H (u, v)  1 e